## Slide 1: BAF Biogeochemical Analytical Facility
Department of Ecology and Environmental Science (EMG)
A part of the KBC infrastructure

## Slide 2: BAF – background
The aquatic research groups at EMG started to build up on existing instrument park for chemical water analyses in 2008, with a TOC-analyzer and a gas chromatograph.
In 2012 the first steps towards a department common instrument park was formed (and the first bills was sent out).
BAF became a part of the KBC-infrastructure in 2017.
By the end of 2017 the existing instrumental facilities came in place.

## Slide 3: BAF
Steering comittee
  Prof. Ann-Kristin Bergström (EMG), manager
  Prof. Jan Karlsson (EMG)
  Prof. Reiner Giesler (EMG)
  Dr. Anders Jonsson (EMG)
  Prof. Jurgen Schleucher (Medical Biochemistry and Biophysics)
  Technician
  Dr. Anders Jonsson

## Slide 4: What do the facility comprise of?
* A number of instruments for wet/dry chemical/biological analyses
- organic carbon
- nutrients
- green house gases
- bacteria/algae nos and biomass
- absorbance/fluorescence
* Some basic laboratory facilities, balances, clean water, autoclave…

## Slide 5: The most important instruments - function and limitations

## Slide 6: BAF – the instrument facilities Can be operated after certificate is taken
TOC analyzer (2017)
FORMACS HT-I (Skalar)
ND 25 detector unit
Primacs module
Autosampler for 80 samples
IR-detector
Chemiluminiscent detector
Substance Detection
TOC 0.1 mg C/L
TN 0.05 mg N/L
POC 15 µg C
DIC 0.1 mg C/L

## Slide 7: BAF – the instrument facilities No certificate can be taken
Nutirent analyzer (2017)
QuAAtro 39 (Seal Analytical)
Segmented flow analyzer
Autosampler 180 samples
Diluter 10-200 times
Digestion unit
Detection
NO3+NO2 0.2 µg N/L
NH4 0.4 µg N/L
PO4 0.3 µg P/L
TN 6 µg N/L
TP 0.4 µg P/L

## Slide 8: BAF – the instrument facilities Can be operated after a certificate is taken
Gas chromatograph (2008)
Clarus 500 (Perkin Elmer)
22 mL sample vials (maximum 10 mL
liquid)
110 samples headspace sampler
Two injector ports
Two capillary Q-Plot columns
N2-carrier gas
FID for CO2/CH4
ECD for N2O (equipped with a make
up gas flow of Ar/5% CH4)

## Slide 9: BAF – the instrument facilities Can be operated after a certificate is taken
Flow Cytometer (2012)
FacsVerse (BD)
Blue and red lasers
Autosampler up to 40 samples/
96 well plate sampler
Manual port 50, 5 or 2 mL tubes
High 120 µL/min
Medium 60 µL/min
Low 12 µL/min
Analyzing
Forward/side scatter and 6 colors
Particles < 50 µm

## Slide 10: BAF – the instrument facilities
Other facilites
Brand
Liquid scintillation counter
(radioactive decay, 14C, 3H) Beckman LS 6500
Fluormeter PerkinElmer LS-55 (with plate reader)
Spectrophotometer Jasco VS-560, (VS-650, autosampler)
Microbalance (0.5 µg) Mettler
Respicond facility (for measuring respiration)
Freeze drier, autoclave, incubation cabinets, muffel furnace...

## Slide 11: Cost for analyses
Price list for analyses (SEK)
The cost for analyses include consumables, maintenance and service + a cost for having samples analyzed by technician.
Instrument Analysis Price
QuAAtro-39 TN/TP 30/element + 25
QuAAtro-39 NO3+NO2/NH4/PO4 20/substance + 25
Formacs HT-I TOC/TN/POC/DIC 30/element +25
FacsVerse Flow cytometer 30/sample + 25
Clarus 500 DIC/CO2/CH4/N2O 30/substance + 25
User fee for other equipments, annual fee (5000 SEK for 1-2 users, 10,000 SEK for 3-5 users, 15,000 SEK for >6 users) or daily fee of 100 SEK/equipment

## Slide 12: Examples

## Slide 13: Examples

## Slide 14: Example

## Slide 15: Questions? anders.jonsson@umu.se